##### DECLARATION OF CONFORMITY

Re: Safety transmitters 3448.004 spec. Ex and 3145.032 spec. Ex.

This electrical apparatus is produced special for use in potentially explosive atmospheres. Sensor type is variable resistor which is a passive component without storage of energy.

Test is not necessary in accordance with the requirements of the European Standards EN 60079.

ATEX Directive 94/9/EC

Certificate of conformity:

Together with an approved Safety Isolated Barriers type 5116B

gurantee HB Products A/S for using this sensor in hazardous area.

[EEx ia]  IIC T5

Security parameter according to Certificate KEMA No 04ATEX1316 X:

Uo	   = 7,5 V

Io	   = 2,2 mA

Lo	   = 1,0H

Co       = 6(F

HB Products A/S

Signed:_________________________

Encl.

El..diagram draw. no. 3448Iex1 or 3145.032Iex1

Certificate for type 5116B signal converter & Safety Barriers